## Slide 1: Virtual Memory: Systems Introduction to Computer Systems

## Slide 2: Today
Virtual memory questions and answers
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 3: Virtual memory reminder/review
Programmer’s view of virtual memory
  Each process has its own private linear address space
  Cannot be corrupted by other processes
System view of virtual memory
  Uses memory efficiently by caching virtual memory pages
    Efficient only because of locality
  Simplifies memory management and programming
  Simplifies protection by providing a convenient interpositioning point to check permissions

## Slide 4: Recall: Address Translation With a Page Table
Virtual page number (VPN)
Virtual page offset (VPO)
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table
Page table base register
(PTBR)
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
Physical page offset (PPO)
0
p-1
Physical page number (PPN)
p
m-1

## Slide 5: Recall: Address Translation: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5

## Slide 6: Question #1
Are the PTEs cached like other memory accesses?
Yes (and no: see next question)

## Slide 7: Page tables in memory, like other data
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
VA: virtual address, PA: physical address, PTE: page table entry, PTEA = PTE address

## Slide 8: Question #2
Isn’t it slow to have to go to memory twice every time?
Yes, it would be… so, real MMUs don’t

## Slide 9: Speeding up Translation with a TLB
Page table entries (PTEs) are cached in L1 like any other memory word
  PTEs may be evicted by other data references
  PTE hit still requires a small L1 delay
Solution: Translation Lookaside Buffer (TLB)
  Small, dedicated, super-fast hardware cache of PTEs in MMU
  Contains complete page table entries for small number of pages

## Slide 10: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3

## Slide 11: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE) Fortunately, TLB misses are rare. Why?

## Slide 12: Question #3
Aren’t the TLB contents wrong after a context switch?
Yes, they would be, so something must be done..
  Option 1: flush TLB on context switch
  Option 2: associate a process ID with each TLB entry

## Slide 13: Question #4
Isn’t the page table huge? How can it be stored in RAM?
Yes, it would be… so, real page tables aren’t simple arrays

## Slide 14: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 64-bit address space, 8-byte PTE
Problem:
  Would need a 32,000 TB page table!
    264 * 2-12 * 23 = 255 bytes
Common solution:
  Multi-level page tables
  Example: 2-level page table
    Level 1 table: each PTE points to a page table (always memory resident)
    Level 2 table: each PTE points to a page (paged in and out like any other data)
Level 1
Table
...
Level 2
Tables
...

## Slide 15: A Two-Level Page Table Hierarchy
Level 1
page table
...
Level 2
page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
32 bit addresses, 4KB pages, 4-byte PTEs

## Slide 16: Translating with a k-level Page Table
VPN-1
0
p-1
n-1
VPO
VPN-2
...
VPN-k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table

## Slide 17: Today
Virtual memory questions and answers
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 18: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag
(bits per field for our simple example)

## Slide 19: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 20: Simple Memory System TLB
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
0
0
0
1
1
0
1
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Translation Lookaside Buffer (TLB)
VPN = 0b1101 = 0x0D

## Slide 21: Simple Memory System Page Table
Only showing the first 16 entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0x0D → 0x2D

## Slide 22: Simple Memory System Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
1
11
0
10
1
9
1
8
0
7
1
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx
1
0
1
0
0
1
V[0b00001101101001] = V[0x369]
P[0b101101101001] = P[0xB69] = 0x15
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
1D
F0
72
36
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B3
B2
B1
B0
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B3
B2
B1
B0
Valid
Tag
Idx

## Slide 23: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36

## Slide 24: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0
0x2E
2
0x0B
N
Y
TBD

## Slide 25: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  CO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem

## Slide 26: Today
Virtual memory questions and answers
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 27: Intel Core i7 Memory System
L1 d-cache
32 KB, 8-way
L2 unified cache
256 KB, 8-way
L3 unified cache
8 MB, 16-way
(shared by all cores)
Main memory
Registers
L1 d-TLB
64 entries, 4-way
L1 i-TLB
128 entries, 4-way
L2 unified TLB
512 entries, 4-way
L1 i-cache
32 KB, 8-way
MMU
(addr translation)
Instruction
fetch
Core x4
DDR3 Memory controller
3 x 64 bit @ 10.66 GB/s
32 GB/s total (shared by all cores)
Processor package
QuickPath interconnect
4 links @ 25.6 GB/s each
To other
cores
To I/O
bridge

## Slide 28: Review of Symbols
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  TLBI: TLB index
  TLBT: TLB tag
  VPO: Virtual page offset
  VPN: Virtual page number
Components of the physical address (PA)
  PPO: Physical page offset (same as VPO)
  PPN: Physical page number
  CO: Byte offset within cache line
  CI: Cache index
  CT: Cache tag

## Slide 29: End-to-end Core i7 Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
4
32
...
L1 TLB (16 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
TLB
miss
TLB
hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1
hit
L1
miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE

## Slide 30: Core i7 Level 1-3 Page Table Entries
Page table physical base address
Unused
G
PS
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page table. Significant fields:
P: Child page table present in physical memory (1) or not (0).
R/W: Read-only or read-write access access permission for all reachable pages.
U/S: user or supervisor (kernel) mode access permission for all reachable pages.
WT: Write-through or write-back cache policy for the child page table.
A: Reference bit (set by MMU on reads and writes, cleared by software).
PS: Page size either 4 KB or 4 MB (defined for Level 3 PTEs only).
Page table physical base address: 40 most significant bits of physical page table address (forces page tables to be 4KB aligned)
XD: Disable or enable instruction fetches from all pages reachable from this PTE.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page table location on disk)
P=0
52
62
63

## Slide 31: Core i7 Level 4 Page Table Entries
Page physical base address
Unused
G
D
A
CD
WT
U/S
R/W
P=1
Each entry references a 4K child page. Significant fields:
P: Child page is present in memory (1) or not (0)
R/W: Read-only or read-write access permission for child page
U/S: User or supervisor mode access
WT: Write-through or write-back cache policy for this page
A: Reference bit (set by MMU on reads and writes, cleared by software)
D: Dirty bit (set by MMU on writes, cleared by software)
Page physical base address: 40 most significant bits of physical page address (forces pages to be 4KB aligned)
XD: Disable or enable instruction fetches from this page.
51
12
11
9
8
7
6
5
4
3
2
1
0
Unused
XD
Available for OS (page location on disk)
P=0
52
62
63

## Slide 32: Core i7 Page Table Translation
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40
/
40
/
40
/
40
/
40
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry

## Slide 33: Cute Trick for Speeding Up L1 Access
Observation
  Bits that determine CI identical in virtual and physical address
  Can index into cache while address translation taking place
  Generally we hit in TLB, so PPN bits (CT bits) available next
  “Virtually indexed, physically tagged”
  Cache carefully sized to make this possible
Physical
address
(PA)
CT
CO
40
6
CI
6
Virtual
address
(VA)
VPN
VPO
36
12
PPO
PPN
Address
Translation
No
Change
CI
L1 Cache
CT
Tag Check

## Slide 34: Virtual Address Space of a Linux Process
Kernel code and data
Memory mapped region
for shared libraries
Runtime heap (malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
%rsp
Process
virtual
memory
brk
Physical memory
Identical for each process
Process-specific data
structs (ptables,
task and mm structs, kernel stack)
Kernel
virtual
memory
0x00400000
Different for each process

## Slide 35: Linux Organizes VM as Collection of “Areas”
vm_next
vm_next
pgd:
  Page global directory address
  Points to L1 page table
vm_prot:
  Read/write permissions for this area
vm_flags
  Pages shared with other processes or private to this process
task_struct
mm_struct
pgd
mm
mmap
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
Text
Data
Shared libraries
0
vm_flags
vm_flags
vm_flags

## Slide 36: Linux Page Fault Handling
read
1
write
2
read
3
vm_next
vm_next
vm_area_struct
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_start
vm_end
vm_prot
vm_next
vm_start
Process virtual memory
text
data
shared libraries
vm_flags
vm_flags
vm_flags
Segmentation fault:
accessing a non-existing page
Normal page fault
Protection exception:
e.g., violating permission by writing to a read-only page (Linux reports as Segmentation fault)

## Slide 37: Today
Virtual memory questions and answers
Simple memory system example
Case study: Core i7/Linux memory system
Memory mapping

## Slide 38: Memory Mapping
VM areas initialized by associating them with disk objects.
  Process is known as memory mapping.
Area can be backed by (i.e., get its initial values from) :
  Regular file on disk (e.g., an executable object file)
    Initial page bytes come from a section of a file
  Anonymous file (e.g., nothing)
    First fault will allocate a physical page full of 0's (demand-zero page)
    Once the page is written to (dirtied), it is like any other page
Dirty pages are copied back and forth between memory and a special swap file.

## Slide 39: Revisiting fork()
Shouldn’t fork() be really slow, since the child needs a copy of the parent’s address space?
Yes, it would be… so, fork() doesn’t really work that way

## Slide 40: Sharing Revisited: Shared Objects
Process 1 maps the shared object.
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory

## Slide 41: Sharing Revisited: Shared Objects
Shared
object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Process 2 maps the shared object.
Notice how the virtual addresses can be different.

## Slide 42: Sharing Revisited: Private Copy-on-write (COW) Objects
Two processes mapping a private copy-on-write (COW) object.
Area flagged as private copy-on-write
PTEs in private areas are flagged as read-only
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Private
copy-on-write
area

## Slide 43: Sharing Revisited: Private Copy-on-write (COW) Objects
Instruction writing to private page triggers protection fault.
Handler creates new R/W page.
Instruction restarts upon handler return.
Copying deferred as long as possible!
Private
copy-on-write object
Physical
memory
Process 1
virtual memory
Process 2
virtual memory
Copy-on-write
Write to private
copy-on-write
page

## Slide 44: The fork Function Revisited
VM and memory mapping explain how fork provides private address space for each process.
  Perfect approach for common case of fork() followed by exec()
To create virtual address for new new process
  Create exact copies of current mm_struct, vm_area_struct, and page tables.
  Flag each page in both processes as read-only
  Flag each vm_area_struct in both processes as private COW
On return, each process has exact copy of virtual memory
Subsequent writes create new pages using COW mechanism

## Slide 45: The execve Function Revisited
To load and run a new program a.out in the current process using execve:
Free vm_area_struct’s and page tables for old areas
Create vm_area_struct’s and page tables for new areas
  Programs and initialized data backed by object files.
  .bss and stack backed by anonymous files .
Set PC to entry point in .text
  Linux will fault in code and data pages as needed.
Memory mapped region
for shared libraries
Runtime heap (via malloc)
Program text (.text)
Initialized data (.data)
Uninitialized data (.bss)
User stack
0
Private, demand-zero
libc.so
.data
.text
Shared, file-backed
Private, demand-zero
Private, demand-zero
Private, file-backed
a.out
.data
.text

## Slide 46: Finding More Shareable Pages
Easy places to identify shareable pages
  Child create via fork
  Processes loading the same binary file
    E.g., bash or python interpreters, web browsers, ...
  Processes loading the same library file
What about others?
  Kernel Same-Page Merging
  OS scans through all of physical memory, looking for duplicate pages
  When found, merge into single copy, marked as copy-on-write
  Implemented in Linux kernel in 2009
  Limited to pages marked as likely candidates
  Especially useful when processor running many virtual machines

## Slide 47: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
Map len bytes starting at offset offset of the file specified by file description fd, preferably at address start
  start: may be 0 for “pick an address”
  prot: PROT_READ, PROT_WRITE, ...
  flags: MAP_ANON, MAP_PRIVATE, MAP_SHARED, ...
Return a pointer to start of mapped area (may not be start)

## Slide 48: User-Level Memory Mapping
void *mmap(void *start, int len,
int prot, int flags, int fd, int offset)
len bytes
start
(or address
chosen by kernel)
Process virtual memory
Disk file specified by
file descriptor fd
len bytes
offset
(bytes)
0
0

## Slide 49: Example: Using mmap to Copy Files
/* mmapcopy driver */
int main(int argc, char **argv)
{
struct stat stat;
int fd;
/* Check for required cmd line arg */
if (argc != 2) {
printf("usage: %s <filename>\n",
argv[0]);
exit(0);
}
/* Copy input file to stdout */
fd = Open(argv[1], O_RDONLY, 0);
Fstat(fd, &stat);
mmapcopy(fd, stat.st_size);
exit(0);
}
Copying a file to stdout without transferring data to user space .
#include "csapp.h"
void mmapcopy(int fd, int size)
{
/* Ptr to memory mapped area */
char *bufp;
bufp = Mmap(NULL, size,
PROT_READ,
MAP_PRIVATE,
fd, 0);
Write(1, bufp, size);
return;
}
mmapcopy.c
mmapcopy.c

## Slide 50: Some Uses of mmap
Reading big files
  Uses paging mechanism to bring files into memory
Shared data structures
  When call with MAP_SHARED flag
    Multiple processes have access to same region of memory
    Risky!
File-based data structures
  E.g., database
  Give prot argument PROT_READ | PROT_WRITE
  When unmap region, file will be updated via write-back
  Can implement load from file / update / write back to file

## Slide 51: Summary
VM requires hardware support
  Exception handling mechanism
  TLB
  Various control registers
VM requires OS support
  Managing page tables
  Implementing page replacement policies
  Managing file system
VM enables many capabilities
  Loading programs from memory
  Forking processes
  Providing memory protection